## Slide 1: Communication policies that shape Embedded Evolution in ESP32 Collectives
Luis Yallico Ylquimiche (SID: 2354065) Supervisor: Dr Paul O'Dowd MSc Robotics 25th August 2025

## Slide 2: Why this research?
Communication is fundamental for swarm behavior emergence
Swarm studies recent focus on co-ordination and task allocation
ESP32 data link (ESP-NOW) has not been explored in swarm literature
Situation of research
Xing A, Celimuge W, Yangfei L, Min L. Multi-Robot Systems and Cooperative Object Transport: Communications, Platforms, and Challenges. 2023. 2644-1268
Internal genetic Algorithm (Local Fitness )
Periodic Migration
Global Convergence Controllers "evolve" Promotes genetic diversity
Rastrigin Function (WIkipedia). 2025.

## Slide 3: What do we address?
Contributions to the field
Aim Quantify the impact of communication policies in a robotic swarm's embedded evolution
1.
Objectives
  Develop a hardware-in-the-loop testbed that permits reliable real-time data capture
  Design set of experiments to systematically test ESP-NOW communication under different independent variables
  Write firmware for the island-model embedded evolution and ESP-NOW
  Evaluate large volumes of data relevant to communication and convergence key performance indicators
2.
Research Question Given the various independent variables profiled, can we identify pragmatic swarm design rules for this type of swarm?
3.
Independent Variable | Implementation
Swarm Density | 3, 8, 13 swarm cohorts
Locomotion | Static vs Brownian motion
Topology Inference | Stochastic peer ordering vs Comm-aware biased peer ordering
Message Limits | Unlimited vs Limited message caps during experiments
Transmission Frequency | Random micro-delays bounded by peer latency to spread out transmission bursts

## Slide 4: Technical Contributions
Hardware-in-the-loop framework
A​
Time (t)
B​
C
D
E​

## Slide 5: Technical Contributions
FreeRTOS GA/ESP-NOW Implementation
Asynchronous
Event push-driven unicast communication
Due to the nature of the communication, we had to handle the execution of the Genetic Algorithm and sending/receiving of messages.
Handle multiple FreeRTOS tasks concurrently and in parallel:
Handle event logging for data analysis
Keep evolving solutions locally
Keep sending and receiving ESP-NOW messages
Use of queues and buffers for in-coming messages.​

## Slide 6: Technical Contributions
I2C Hardware Abstraction Layer (HAL) bug fixing for ESP32
https://github.com/espressif/esp-idf/issues/680#issuecomment-2426425417
Successfully modified ESP-IDF HAL source code to implement I2C and became an open-source contributor.

## Slide 7: Knowledge Contributions
Link formation and transmission timing, drive QoS and adaptation on this platform
Topology Inference
Transmission Frequency

## Slide 8: Knowledge Contributions
Link formation and transmission timing, drive QoS and adaptation on this platform
Topology Inference
Transmission Frequency

## Slide 9: Knowledge Contributions
13-agent deep dive

## Slide 10: Knowledge Contributions
Conclusions and Future Studies
Research Question Given the various independent variables profiled, can we identify pragmatic swarm design rules for this type of swarm?
Design Rules
Rapid diffusion / high throughput → stochastic + micro-delays.
Low latency/jitter / robustness → comm-aware (limit effective links).
Future Work Stress-test larger and dynamic payloads to probe the limits of our conclusions. Determine optimal communication policies for energy efficient deploymens